Sending commands

Usage:
[instruction] [parameter] [LF]

Where:
instruction is a single character defining the instruction
parameter is an ASCII integer
LF is the line feed character, '\n' or 0x0A

List of instructions:
Character	Name	Parameter	Description	Response
@	Init	None	Initialises the controller, establishes communications with Cnc and Dcell.	@1
^	Save	None	Saves parameters to EEPROM (currently only for Cnc parameters)	^1
#	Log	None	Toggles logging on/off	#[value]
!	DoProbe	(0, 1)	Performs a probe, returning force readings. Parameter of 1 indicates a downward move, 0 indicates an upward move.	*[depth],[force] / !0 or !1
*	Data	None	Reserved for use when returning force readings.
,	DataSeparator	None	Reserved for use when returning force readings.
z	DoRefHome	None	Performs a reference homing cycle.	Z1
e	SetEStop	(0, 1)	Sets the emergency stop signal. If 1, the controller will stop any task currently running; this must be reset to 0 in order to resume operation.	E[value]
g	SetGroundLevel	mm*0.1	Sets the ground level. This is the distance between the ground and the tip of the probe in its home position.	G[value]
t	SetTopSpeed	mm/s	Sets the top speed.	T[value]
s	SetSpeed	mm/s	Sets the working speed. This must be less than the top speed.	S[value]
k	SetHomeSpeed	mm/s	Sets the axis homing speed. This must be less than the top speed.	K[value]
a	SetAccel	mm/s^2	Sets the acceleration rate.	A[value]
d	SetDecel	mm/s^2	Sets the deceleration rate.	D[value]
l	SetProbeDepth	mm*0.1	Sets the depth of a downward probe relative to ground level.	L[value]
q	SetDistPerReading	mm*0.1	Sets the distance between force readings.	Q[value]
r	SetLFDTolerance	cs	Sets the amount of time the LFD needs to trigger for before an estop is thrown. 0 ignores the LFD.	R[value]
p	SetEnable	(0, 1)	Sets the “Motor Enable” (Power) signal.	P[value]
m	SetMaxForce	N	Sets the maximum force before an estop is thrown. This must be greater than the minimum force.	M[value]
n	SetMinForce	N	Sets the minimum force before an estop is thrown. This must be less than the maximum force.	N[value]
x	SetMaxForceDelta	N	Sets the maximum force increase between readings before an estop is thrown.	X[value]
y	SetMinForceDelta	N	Sets the maximum force decrease between readings before an estop is thrown.	Y[value]
v	SetForceDeltaAbs	(0, 1)	Sets whether force delta operates on signed forces (0) or absolute forces (1).	V[value]
o	SetSafeDisconnect	(0, 1)	Sets whether the controller losing communication with the robot should try to retract the probe automatically.	O[value]
f	ClearError	0	Clears any currently active errors.	F[value]
b	CncPassthrough	None	Disables the controller and sends all input directly to Cnc. The controller must be reset to resume operation.	[none]
c	DCellPassthrough	None	Disables the controller and sends all input directly to Dcell. The controller must be reset to resume operation.	[none]
Z	IsRefHomed	None	Returns whether a “Reference Home” cycle has been performed.	Z[value]
E	GetEStop	None	Returns the current Estop state.	E[value]
G	GetGroundLevel	None	Returns the ground level.	G[value]
T	GetTopSpeed	None	Returns the top speed.	T[value]
S	GetSpeed	None	Returns the working speed.	S[value]
K	GetHomeSpeed	None	Returns the homing speed.	K[value]
A	GetAccel	None	Returns the acceleration rate.	A[value]
D	GetDecel	None	Returns the deceleration rate.	D[value]
L	GetProbeDepth	None	Returns the probe depth.	L[value]
W	GetForce	None	Returns a force reading.	W[value]
Q	GetDistPerReading	None	Returns the distance between force readings.	Q[value]
R	GetLFDTolerance	None	Returns the amount of time the LFD needs to trigger for before an estop is thrown.	R[value]
P	GetEnable	None	Returns the “Motor Enable” (Power) signal.	P[value]
M	GetMaxForce	None	Returns the maximum force before an estop is thrown.	M[value]
N	GetMinForce	None	Returns the minimum force before an estop is thrown.	N[value]
X	GetMaxForceDelta	None	Returns the maximum force increase between readings before an estop is thrown.	X[value]
Y	GetMinForceDelta	None	Returns the maximum force decrease between readings before an estop is thrown.	Y[value]
V	GetForceDeltaAbs	None	Returns whether force delta operates on signed forces (0) or absolute forces (1).	V[value]
O	GetSafeDisconnect	None	Returns whether the controller losing communication with the robot should try to retract the probe automatically.	O[value]
H	GetHomeState	None	Returns the home state of the motor.	H[value]
U	GetLFDState	None	Returns the state of the LFD (0 = off, 1 = on).	V[value]
J	GetProbeState	None	Returns the state of the probe (0 = at home, 1 = not at home).	J[value]
F	GetError	None	Returns any currently active errors.	F[value]

For example:
@	Initialises the system, returns “@1” to indicate a successful initialisation.
m200	Sets the maximum allowed force to 200N, returns “M200” to confirm.
!1	Performs a downward probe, returns “!1” to indicate a successful probe.
W	Returns the current force, returns “W100” if the current force is 100N.

If an estop or error is active, or the probe is moving, only Init, SetEStop, SetError, GetEStop, and GetError will be acted upon.

Attempting to perform another task while estop is active will return “E1”. Attempting to perform another task while an error is active will return the currently active error code. Attempting to perform another task while the probe is moving will return a BUSY error. In order to continue operations after an error, errors should be cleared using “f0”, and then the estop should be cleared using “e0”.

Responses are transmitted by the controller as soon as the relevant actions have been completed; parameter setters and getters should have very little delay (variable depending on communication with other parts of the system), but commands that require movement (DoRefHome ('z') and DoProbe ('!')) will only return their expected response once the movement is completed.

After a DoProbe ('!') command is issued, the controller will return a series of readings in the form of “*[depth],[force]”. A negative depth means the probe is above ground. The distance between readings can be adjusted using DistPerReading ('q'/'Q'); it will usually be necessary to adjust MaxForceDelta ('x'/'X') and MinForceDelta ('y'/'Y') at the same time, as these are based on the difference between two consecutive readings.

Safety features

An manual estop can be thrown by the robot at any time by sending a SetEStop command (“e1”).

LFDTolerance ('r'/'R') determines how long the Lateral Force Detector should be triggered for before throwing a LIMIT EXCEEDED error (and estop). This should be set as low as possible without throwing false positives, but can be turned off entirely by setting to 0.

MaxForce ('m'/'M') and MinForce ('n'/'N') determine how much force the probe should take before throwing a LIMIT EXCEEDED error (and estop). MaxForce should be set higher than expected limits, but lower than operational limits; MinForce should be set to the negative of MaxForce. Note that when recovering from an error, MaxForce should be raised to allow the probe to become unstuck from any terrain it may have become embedded in.

MaxForceDelta ('x'/'X') and MinForceDelta ('y'/'Y') further protect the probe by stopping if there's a sudden change in force, throwing a LIMIT EXCEEDED error. These can be modified to detect changes in absolute or relative force using ForceDeltaAbs ('v'/'V').

Before driving off, check that the probe is fully retracted from the ground by issuing a GetProbeState ('J') command. A value of 0 means the probe is fully retracted and it is safe to drive off; a value of 1 means the probe may be in or close to the ground, and returning the probe to its home position (DoProbe 0 (“!0”) if no error occurred, or DoRefHome ('z')) is strongly recommended.

If the controller has not received any input for three seconds, it will assume communication has been lost and throw a NO COMMS error. If SafeDisconnect ('o'/'O') is set to 1, it will try to refhome first. When sending the controller a space (followed by the line feed character), the controller will acknowledge by echoing it back, resetting the timer without performing any actions.

Standard initialisation sequence

“@” (repeat if fails) to tell the controller to gather information from the rest of the system
“f0\ne0\np1” to clear errors and estop and enable power
Set remaining parameters as needed
Refhome

List of errors:
Number	Name	Parameter	Cause
0	NONE	' '	Normal behaviour. (no Estop)
1	ESTOP	'e'	The emergency stop was manually activated, or activated from an unknown part of the system.
2	UNRECOGNISED INSTRUCTION	[ins]	The instruction was not recognised as a valid instruction. (no Estop)
3	BUSY	[ins]	The instruction was rejected because the controller is currently performing another task. (no Estop)
4	STATE	[ins]	The instruction was rejected because the controller is not in the right state to perform the task. (no Estop)
5	PARAMETER	[ins]	The parameter value is not within the valid range for that parameter. (no Estop)
6	LIMIT EXCEEDED	[sys]	Part of the system exceeded the defined limits.
7	HARDWARE FAULT	[sys]	Part of the system developed a fault, which may be fixed with a power cycle.
8	HARDWARE FAILURE	[sys]	Part of the system failed.
9	NO COMMS	[sys]	Communication with a part of the system failed.
':'	UNKNOWN	' '	An unknown error occurred.

Where:
[ins] is the instruction code that caused the error
[sys] is a single character defining the part of the system involved
Character	System part
m	Motor
l	Lateral Force Detector
f	Dcell (force limit exceeded)
d	Dcell (force delta limit exceeded)
c	Dcell
b	Cnc
a	Controller

For example:
F1e	An estop was thrown either manually or by an unknown part of the system.
F4!	The probe could not be performed because the system is in the wrong state.
F6l	The Lateral Force Detector exceeded the set tolerance level.
F9c	Communication with Dcell failed.

In order to continue operations after an error, errors should be cleared using “f0”, and then the estop should be cleared using “e0”.